## Slide 1
KANDA
A Multimodal Embodied Robot Agent
Powered by Large Language Models
Review I · Phase 2: Embodiment Layer
Hardware-Aware Autonomous Control System
PHASE 2 ✅

## Slide 2
Agenda
Review I · Kanda Robot Project
01
Introduction
02
Conceptual Understanding
03
Revisiting Objectives
04
Tool / Technique Selection & Justification
05
Solution Design Quality
06
Innovation & Problem-Solving
07
Partial Implementation
08
References

## Slide 3
Introduction
What is Kanda?
Kanda is a hardware-grounded robotic agent designed to evolve from a rule-based autonomous controller into a fully LLM-driven embodied AI system — integrating physical sensing, motor control, and natural language reasoning.
Problem Gap
✗ Existing robots are purely rule-based
✗ No integration of AI reasoning with physical hardware
✗ Limited adaptability to novel environments
✗ Multimodal input (vision/audio) largely absent
Proposed Solution
✓ Embodied robot with full sense–decide–act loop
✓ LLM as reasoning brain (Raspberry Pi bridge)
✓ Multimodal inputs: ultrasonic, camera, microphone
✓ Hardware-aware action generation via structured JSON
✓ Closed-loop feedback with real-time OLED display

## Slide 4
Conceptual Understanding
Embodied AI · Reactive vs Deliberative Agents
Embodied AI
• Intelligence that exists within a physical body
• Perception → Action loop is central
• Grounded in real-world sensor feedback
• Contrast: disembodied LLMs act on text only
Reactive Agent (Current)
• Responds directly to sensor inputs
• No internal world model
• Fast, deterministic, hardware-safe
• Limited — cannot generalize to new tasks
Deliberative Agent (Target)
• Builds context before acting
• Uses LLM for reasoning & planning
• Can handle open-ended instructions
• Slower but far more capable

## Slide 5
Revisiting Objectives
Original Goals vs Current Status
#
Objective
Implementation Detail
Status
1
Build a stable hardware platform
Design stable power + sensor + motor system
✅ Done
2
Real-time obstacle detection
3× HC-SR04 sensors with voltage dividers
✅ Done
3
Autonomous navigation logic
Sense→Decide→Act loop with smooth steering
✅ Done
4
Real-time visual feedback
SSD1306 OLED showing distances + decisions
✅ Done
5
Clean, conflict-free pin mapping
Avoided strapping/UART/unstable GPIO pins
✅ Done
6
Integrate LLM reasoning layer
Raspberry Pi bridge + LLM API pipeline
⏳ Planned
7
Multimodal input (camera, mic)
Camera + microphone module integration
⏳ Planned
8
Hardware-aware JSON action generation
Structured command protocol: Pi → ESP32
⏳ Planned
9
Closed-loop LLM feedback
Sensor telemetry fed back to LLM context
⏳ Planned

## Slide 6
Tool / Technique Selection & Justification
Hardware + Software stack decisions
ESP32
Microcontroller
Dual-core, built-in WiFi/BT, 3.3V, abundant GPIOs, ledc PWM API
TB6612FNG
Motor Driver
Efficient H-bridge, 1.2A/ch, STBY pin, direction + PWM control
HC-SR04 ×3
Ultrasonic Sensor
Low cost, 2–400cm range; 1kΩ+1kΩ divider for 5V→2.5V ECHO
SSD1306 OLED
Display
I2C (2 pins), 128×64, real-time decision feedback
Buck Converter
Power Regulation
Stable 5V for ESP32; motors run on direct battery to avoid surge
Raspberry Pi
AI Compute Bridge
Full Linux OS, runs Python, calls LLM API, UART to ESP32
GPT-4 / Gemini
LLM Reasoning
Multimodal capability, function calling for structured JSON output
JSON Protocol
Command Interface
Type-safe, validatable, hardware-safe action specification

## Slide 7
Solution Design — High-Level Architecture (HLD)
Full system view: completed (green) · planned (gray)
⚙️ Phase 2 — Embodiment Layer ✅
HC-SR04 (×3)
Front · Left · Right ultrasonic
ESP32 DevKit
Central microcontroller
TB6612FNG
Dual motor driver
SSD1306 OLED
I2C real-time display
LiPo + BMS + Buck
Stable power architecture
Left + Right Motor
Physical locomotion
🧠 Phase 3 — Intelligence Layer ⏳
Camera Module
Visual perception input
Microphone
Audio / speech input
Raspberry Pi
AI compute bridge (brain)
LLM API
GPT-4 / Gemini reasoning
Safety Validator
Command verification layer
Speaker (TTS)
Audio output / feedback
UART

## Slide 8
Solution Design — Low-Level Design (LLD)
Pin mapping · Power architecture · Signal conditioning
ESP32 Pin Mapping
GPIO
Function
GPIO 5
TRIG_F (Front HC-SR04)
GPIO 34
ECHO_F [input-only, 2.5V divider]
GPIO 13
TRIG_L (Left HC-SR04)
GPIO 35
ECHO_L [input-only, 2.5V divider]
GPIO 4
TRIG_R (Right HC-SR04)
GPIO 32
ECHO_R [2.5V divider]
GPIO 18
AIN1 — Motor A dir
GPIO 19
AIN2 — Motor A dir
GPIO 23
PWMA — Motor A speed
GPIO 26
BIN1 — Motor B dir
GPIO 27
BIN2 — Motor B dir
GPIO 14
PWMB — Motor B speed
GPIO 21
SDA — OLED I2C
GPIO 22
SCL — OLED I2C
GPIO 1/3
UART TX/RX → Raspberry Pi
Power Architecture
LiPo Battery 7.4V
BMS (protection)
Main Switch
Buck Converter → 5V
ESP32 VIN
TB6612FNG VM
Motors (L+R)
Raspberry Pi ⏳
★ All grounds tied together (common GND)
★ Capacitors across motor rails — suppress voltage spikes
★ Motors NOT powered through buck (current surge protection)

## Slide 9
Flow Diagram — Sense → Decide → Act
Current: rule-based (green) · Planned: LLM-driven (gray)
Current Implementation ✅
⚡ Power On & Init
Read F / L / R Distances
Front < 20 cm?
Stop Motors · 200ms
Left > Right? → Turn L / R
Left < 15 cm? → Slight Right
Right < 15 cm? → Slight Left
FORWARD at speedVal
Update OLED + Serial log
Delay 100ms → loop
Planned: LLM-Driven ⏳
Camera + Mic + Sensor Input
Build Multimodal Context
LLM API Call (Raspberry Pi)
Parse JSON Command
Safety Validation
Serial → ESP32
Execute Motor Command
Sensor telemetry → Pi (loop)
Phase 3

## Slide 10
Use Case Diagram
Actor → System interactions · completed (green) · planned (gray)
👤 User / Engineer
🌍 Environment (Physical)
🤖 LLM Service (API)
Kanda Robot System
Flash Firmware to ESP32
Monitor via Serial + OLED
Tune Speed / Threshold Params
Autonomous Obstacle Avoidance
Real-time Sensor Display
Give Voice / Text Command
Camera Scene Understanding
LLM Reasoning & Decision
Natural Language Action
Safety Override / Validation
✅ Completed
⏳ Planned

## Slide 11
Innovation & Problem-Solving
Engineering decisions that made the system work
Hardware-First AI Foundation
• Built full embodiment layer before AI to ensure stable execution substrate
• Most academic projects bolt hardware onto AI — we invert this correctly
• Result: deterministic, safe motor control regardless of AI state
Voltage Divider Improvisation
• HC-SR04 ECHO outputs 5V — unsafe for ESP32 3.3V GPIO
• No 2kΩ resistors available → used 1kΩ + 1kΩ (same ratio, same result)
• Demonstrates engineering principle: workable + safe > perfect
ESP32 Core v3 API Migration
• ledcSetup() deprecated in Arduino core v3 — caused compile errors
• Migrated to new ledcAttach(pin, freq, bits) single-call API
• Proactively future-proofed against further deprecation
Dual-Layer Architecture (Body/Brain)
• ESP32 = Body: fast, deterministic hardware execution
• Raspberry Pi = Brain: LLM reasoning, context, planning
• Separation allows independent testing and safe fallback

## Slide 12
Partial Implementation — Phase 2 Complete
What is built · tested · and working now
✅ Completed & Working
Power Architecture
Battery → BMS → Buck → ESP32 (motors direct)
3× HC-SR04 Sensors
Voltage dividers on ECHO · GPIO34/35/32
TB6612FNG Motor Driver
AIN/BIN direction + PWMA/PWMB speed control
SSD1306 OLED
I2C on GPIO21/22 · real-time sensor + action display
Obstacle Avoidance Logic
Front threshold · side steering · smooth turning
Pin Mapping
Conflict-free · no strapping/UART/unstable pins
ESP32 Core v3 Firmware
ledcAttach() API · serial debug output
⏳ Pending — Phase 3
Raspberry Pi Integration
UART bridge ESP32↔Pi · JSON command protocol
Camera Module
Video frames → Pi → LLM context
Microphone
Audio input · speech-to-text pipeline
LLM API Pipeline
Prompt engineering · GPT-4/Gemini integration
Safety Validator
Command range checks before motor execution
Speaker / TTS
Audio feedback from robot
Closed-Loop Telemetry
Sensor data fed back into LLM context

## Slide 13
References
[1] Espressif Systems. (2024). ESP32 Technical Reference Manual. https://docs.espressif.com
Hardware datasheet for ESP32 microcontroller
[2] Toshiba. (2020). TB6612FNG Dual DC Motor Driver Datasheet.
Motor driver component specification
[3] JSR. HC-SR04 Ultrasonic Module User Guide.
Ultrasonic sensor operational parameters
[4] Solomon Systech. SSD1306 OLED Datasheet.
128×64 OLED display I2C communication protocol
[5] Brown, T., et al. (2020). Language Models are Few-Shot Learners. NeurIPS.
Foundation paper on GPT-3 / LLM capabilities
[6] Ahn, M., et al. (2022). Do As I Can, Not As I Say: Grounding Language in Robotic Affordances. arXiv:2204.01691.
SayCan — embodied AI with LLM reasoning
[7] Brohan, A., et al. (2023). RT-2: Vision-Language-Action Models Transfer Web Knowledge to Robotic Control. arXiv:2307.15818.
Multimodal LLM-to-robot action transfer
[8] Peng, X., et al. (2023). EmbodiedGPT: Vision-Language Pre-Training via Embodied Chain of Thought. arXiv:2305.15021.
Chain-of-thought reasoning for embodied agents
[9] Arduino. (2024). ESP32 Arduino Core v3 Migration Guide. https://docs.arduino.cc
ledcAttach API changes from core v2 to v3

## Slide 14
Thank You
Kanda · A Multimodal Embodied Robot Agent
Phase 2 Complete · Foundation ready for LLM Integration
Hardware Platform ✅
Obstacle Avoidance ✅
OLED Feedback ✅
LLM Integration ⏳
Multimodal Input ⏳